## Slide 1
Loss of spatial detail due to limited resolving power of imaging optics
a point object/source does not produce point image
increasing the megapixel count AND/OR shrinking the size of a pixel does not solve the problem
Loss of absolute size & shape information due to projection
O mnifocus image synthesis using Lens Swivel
Indranil Sinharoy Prasanna Rangarajan Marc P. Christensen
isinharoy@smu.edu prangara@smu.edu mpc@lyle.smu.edu
Create an all-in-focus image by fusing multiple images taken under lens rotations? It’s all about the pupils!
Photonics Architecture Lab, Lyle School of Engineering, Southern Methodist University, Dallas, Texas, USA.
Introduction
An omnifocus image has everything in the close foreground to far background in sharp focus.
Lenses can focus only on a single surface—usually, the plane of sharp focus—as dictated by the laws of physics. Consequently, objects fore and aft the plane of sharp focus gradually get out of focus and appear blurry in the image. This interplay of light and lenses leads to the limited depth of field problem.
Several methods overcome this problem. For example, wavefront coding, plenoptic imaging, Scheimpflug imaging, focus stacking, etc.
In Scheimpflug imaging the lens or the sensor or both are rotated, which induces a rotation of the plane of sharp focus allowing scenes with significant depths to be in focus.
Depth of field
Lens plane
Sensor plane
Plane of sharp focus
In focus stacking, images are captured at multiple focus depths. Therefore, regions only at specific depths are in focus in a single image. Collectively, however, the stack contains the whole scene in focus distributed amongst the images.
An omnifocus image is created by registering the images, followed by identifying and blending the in-focus regions.
DEEP OBJECT SPACE
Sensor translation
depth of field
5…1
1
5
The entrance and exit pupils are the images of the limiting aperture. The entrance pupil is the center of projection in the object side.
The pupil magnification,
Geometric model
Relation between object point and image point :
Inter-image homography for lens tilt about the entrance pupil, if & are corresponding points:
,
,
3
1
2
The corresponding points between two images obtained under different lens rotations are related by a transformation called the inter-image homography.
SENSOR PLANE
y
x
z
Meridional Plane
OPTICAL AXIS (OA)
y
x
z
SAGITTAL Plane
Entrance pupil
Exit pupil
Chief ray
Pivots
: 3rd column of (optical axis).
, : Camera and Image coordinate frames. Origin of is coincident of the pivot.
, : Center of entrance & exit pupils resp.
: Normal to sensor plane.
: Rotation matrix; orientation of lens plane.
, : Loc. of ent. & exit pupils resp. from the pivot.
: Rotation matrix; orientation of sensor plane.
: Distance of image plane from pivot.
If pupil magnification, the inter-image homography between the reference image (for no lens tilt) and an image obtained under a lens rotation of , reduces to a simple scaling & translation transformation:
4
Inter-image homography,
5
6
Further, to focus on an object plane at a distance (measured from the entrance pupil) and tilted by an angle about the x-axis by rotating the lens (about its entrance pupil), the following conditions must be satisfied:
Image plane distance:
The object plane tilt is related to the lens plane tilt angle as:
Substituting and in Eq. :
Sensor plane
Optical axis
Lens plane
Object plane
6
7
The above quadratic curve expression can be used to determine for known values of .
Simulation in Zemax with PyZDDE
-axis
200 mm
800 mm
200 mm
89 mm
64 mm
13 tilts
between -8° & +8°
6x5 sq. mm, 1.78
Sensor plane
Lens (=1)
Paraxial thick-lens model with spherical aberration;
= 24 mm, F/2.5
1/13 (0°)
1/2
1/2
7/13 (-8°)
1/2
1/2
13/13 (8°)
1/2
1/2
Sensor image
Focus measure
The top left figure shows the setup of a simulation in Zemax in which a 24 mm, F/2.5 symmetric lens (=1) was used to image three playing cards for 13 lens rotations of the lens about the entrance pupil. We have shown 3 (out of 13) images of the scene as it appears on the sensor above. Notice the transverse shift in the image field between the images as predicted by Eq. . The in-focus regions of the scene, detected using a Laplacian of Gaussian filter, are also shown above. Notice when the lens is tilted, portions of all three cards in focus.
Following precise registration of the images in the stack using the inter-image homography H, we selectively blend the portions of the scene that are in focus to create a composite image in which all three cards appear sharp.
Schematic of setup
4
Registration
Composite image
Focus measure (LoG)
Blending
1/13, , Reference image.
7/13, , Image field shifted and scaled with respect to the reference image.
13/13, , Image field shifted and scaled with respect to the reference image.
Discussion
Advantages and comparison with frontoparallel focus stacking
The registration using closed form equation is simple, esp. if the pupil magnification of the lens is one.
Can be used to improve the depth of field around a tilted object plane in Scheimpflug imaging.
What if the pupil magnification of the lens is different from one?
The rotation of the lens induces a shift and scaling of the image field. If the pupil magnification is one, the scaling is uniform and the shift is simple. If the pupil magnification is different from one, then anisotropic shift across the image field manifests as image distortion.
What if we rotate the lens about a point away from the entrance pupil?
If the lens is rotated about a point away from the entrance pupil then amount of shift experienced by points in the image field is dependent on depth (parallax). Then, registering becomes hard.
Coincident grid of image points from two planes at different depths.
The top, middle and bottom rows of the grid, following lens rotation.
The top, middle and bottom rows of the grid, following lens rotation.
What if need to increase the depth of field just around a tilted object surface of known tilt angle ?
First we need to determine the required lens rotation angle . While Eq. Y yields in terms of , obtaining an inverse relationship for given is hard. Instead, we use Eq. which yields a quadratic curve for the given parameters. The lens tilt is then obtained as the intersection of the quadratic curve and the unit circle as shown to the right.
6
7
The top, middle and bottom rows of the grid, following lens rotation about a point away from the entrance pupil.
The top, middle and bottom rows of the grid, following lens rotation about a point away from the entrance pupil.
Acknowledgements
[1] C. H. Anderson, J. R. Bergen, P. J. Burt, J. M. Ogden, “Pyramid Methods in Image Processing,” RCA Engineer, vol. 29, pp. 33-41 (1984).
[2] Jacobson, Ralph, Sidney Ray, Geoffrey G. Attridge, and Norman Axford, Manual of Photography (Taylor & Francis, 2000), Chap. 10.
[3] Indranil Sinharoy, Prasanna Rangarajan, and Marc P. Christensen, “Geometric model of image formation in Scheimpflug cameras,” PeerJ
Preprints 4:e1887v1 https://doi.org/10.7287/peerj.preprints.1887v1 (2016).
[4] Indranil Sinharoy et al., PyZDDE: Release version 2.0.2. Zenodo. 10.5281/zenodo.44295 (2016).
[5] Open source tools:
indranilsinharoy.com/projects/omnifocus