## Slide 1
Scheimpflug with Computational Imaging to Extend
the Depth of Field of Iris Recognition Systems
Please help yourself with some cookies, brownies and soft drinks.
Thank you.
Dr. Marc P. Christensen
Dr. Delores M. Etter
Dr. Dinesh Rajan
Dr. Panos Papamichalis
Dr. Yunkai Zhou
Indranil Sinharoy
Committee:
Notes: Good afternoon everyone. Thanks so much for taking the time out of your day to attend my thesis defense

## Slide 2
0.000000000000000000000000000000000000000000000000000000000000000000000001
Unique
[Photographs by Jon Miles, milesresearch.com]
Notes: That’s 71 zeros between the decimal point and the one. That’s the probability that two irises, the colored tissue surrounding the pupils in the eyes, picked at random, will exactly match. That is how staggeringly unique each iris pattern is … but that’s not all.

## Slide 3
[Photograph by Suren Manvelyan, surenmanvelyan.com]
Several desirable properties of the iris pattern make it an ideal biometric
Unique
Stable over time
Protected by the cornea from tampering
Easily accessible
Notes: Other properties such as stability over time, protection from accidental and intentional tampering and easy accessibility make the iris pattern an ideal biometric.

## Slide 4
[Roger Cornfoot [CC BY-SA 2.0 (http://creativecommons.org/licenses/by-sa/2.0)], via Wikimedia Commons]
Iris recognition technology has great potential for providing robust surveillance
Notes: In recent years, public safety concerns have increased significantly. There is a huge demand for robust surveillance in large, uncontrolled environments to provide public safety.
And iris recognition technology has the potential for providing such robust and automated surveillance.
But there is a problem!

## Slide 5
[CANPASS Air Iris Recognition System, biometricwatch.com, 2007]
[AOptix Technologies, Inc, asis.confex.com/asis/ansem2010/webprogram/Session24387.html]
[Hoyos Corp. & Stanley CSS demo., Photo by Geoff Kohl, Security InfoWatch, 2011]
Hitherto, iris recognition has been restricted to close-range & well-controlled spaces
Notes: Despite the fact that iris recognition has been used successfully in close range and restricted environments, it has failed to gain wide scale adoption in large, open, unrestricted, public spaces.
The problem arises due to a fundamental limitation of all imaging systems—the depth of field (DOF)!

## Slide 6
The depth of field (DOF) is the limited range of distances in the scene within which subjects appear sharp in the image
Gaussian formula:
Aperture stop
Image plane
Lens elements
Lens elements
DOF
Shallow DOF
Large DOF
F/5.6
F/8
F/11
F/16
F/22
Plane of sharp focus (PoSF)
Notes: Here is a schematic of a typical lens-- consisting of elemental lenses on both sides of an aperture. The aperture is an opening that is used to control the amount of light passing through the lens.
[Click]
The Gaussian lens formula, which we are all aware of, implies that only one plane in the object space can be in focus. Subjects away from the plane of sharp focus progressively begins to blur more and more.
[Click]
The range of distances in the object space within which subjects appear relatively sharp, is called the depth of field (DOF).
[Click]
In traditional cameras, the DOF is controlled by changing the size of the aperture. Larger apertures result in smaller DOF and smaller apertures result in larger DOF. The relative size of the apertures in a lens are designated using something called the F-number. Small F-number means larger aperture and shallow DOF, larger F-number means smaller aperture and larger DOF.
[I need to be very clear about mentioning that the F/# are ratios, the value depends on the diameter ]

## Slide 7
In traditional cameras the DOF is usually controlled by the aperture
Shallow DOF, aperture: F/2.8
Large DOF, aperture: F/32
Notes: Here is an example of an image with very shallow DOF.
[Click]
And here is an image with a large DOF obtained by making the aperture smaller… reducing the area by almost a factor of 256.
But if we can get a large DOF by using a smaller aperture, then why don’t we use a small aperture for extending the DOF of iris recognition systems?
There are a number of reasons, and here is one:
[[The clocks appear]]
It took over two orders of magnitude more time to capture the image on the right. While that’s probably OK for inanimate beings, it is surely unacceptable for sentients going about their daily business. Moreover, we run into the typical tradeoff of optical imaging

## Slide 8
It is impossible to get high resolution, large DOF & high SNR simultaneously
in traditional imaging
Notes: Here are three images of the same scene. The
The first one obtained with an large aperture.
[CLICK]
It has limited

## Slide 9
Increasing the DOF of the iris camera is an effective way of increasing the capture volume
L
H
W
Standoff distance
Capture volume
Notes: The capture volume is the three dimensional region within which we can acquire high quality images of the iris suitable for iris recognition. The width and height of the capture volume is primarily determined by the field of view of the camera. Therefore, they can be increased by increasing the sensor dimensions. However, the only way to increase the capture volume axially along its length is by improving the DOF of the iris camera.
Note that the standoff distance can be improved by using a higher magnification lens.

## Slide 10
The goal in this work is to extend the capture volume of iris recognition systems
What is an ideal solution?
Extend the capture volume significantly (comparable or better than existing solutions)
Scalable
Low computational complexity for real time operation
Low cost
Notes: State the goals here?

## Slide 11
The original contributions of this thesis
New pair of general imaging models
  Lens and the sensor planes can freely rotate about independent pivots
  Pupil parameters enable accurate and efficient estimation of geometric image properties
A new computational imaging approach for extending the depth of field of imaging systems
Conference paper, Imaging and Applied Optics Congress 2016
  Won Best Multimedia Award ( )
Journal paper submitted to OSA Applied Optics (stage: in peer review)
Software library for automating and externally controlling optical design and simulation tasks in Zemax
Invention disclosure (stage: patent being written by a lawyer)
Notes: In the course of solving the limited capture volume problem in iris recognition, I made a few contributions of my own
…
…
In addition, I am currently working on two conference papers :
* IEEE International Conference on Computational Photography 2017, and
* IEEE International Joint Conference on Biometrics 2017,

## Slide 12
Background
The new models
New comp. imaging method: Angular Focus Stacking (AFS)
Zemax simulation
Experimental results
Notes: The rest of the presentation is structured as follows
When we I talk about the new models, I will talk about the verification process, and some of the consequences.
Following which I will introduce to you the new computational imaging approach, which we call the Angular Focus Stacking for extending DOF
A simulation to demonstrate the theory of Angular Focus stacking, created in Zemax
Finally, I will show you some experimental results that proves, that the technique does work with real cameras.

## Slide 13
Existing solutions for extending the capture volume are either costly or plagued by noise
Two main class of solutions:
Multiple field of view stitching over space and/or time are costly
Wavefront coding—e.g. Cubic Phase Mask—exhibit low SNR at high spatial frequencies
Notes: When we started looking into this problem, the first thing we did, as researchers would do is look at the existing solutions.
I found out that although there are slight differences between each approach, they can be broadly classified into two techniques:
Approaches that use multiple cameras with multiple focal lengths and or with Pan-Tilt-Units to augment the field views over time and space.
Computational imaging approaches—mostly wavefront coding--to extend the instantaneous DOF.
In addition, most existing solutions also use video on top of the either method.
While the former methods are usually costly to install, maintain and scale, the later methods are afflicted by noise, especially near the high spatial frequencies.

## Slide 14
Notes: [Blank slide]
After thinking about various ways to approach the problem, for example, using light field cameras, … we decided to invest our resouces on employing the Scheimpflug technique along with some computational processing.

## Slide 15
The lens & sensor in a Scheimpflug camera can rotate about independent pivots
Notes: Here is an image of a Scheimpflug camera. The thing that makes a Scheimpflug camera, also known as View camera, different from conventional cameras, is that
[CLICK]
the lens and sensor are free to rotate about their independent pivots.
[CLICK]

## Slide 16
The lens & sensor in a Scheimpflug camera can rotate about independent pivots

## Slide 17
Scheimpflug principle: Rotating the lens or the sensor also rotates the plane of sharp focus
Optical axis
Plane of sharp focus (PoSF)
Depth of field (DOF)
Sensor
Plane of sharp focus (PoSF)
Optical axis
Depth of field (DOF)
Sensor
Notes: [Explain the DOF of frontoparallel camera]
[CLICK]
[Explain what happens in a Scheimpflug camera]

## Slide 18
Notes: [Blank??]
So, after researching in the market, we invensted on buying a very good Scheimpflug camera, for Sinar a company that prides itself on Swiss engineering.
I was awestruck by the beauty of this gadget.

## Slide 19
1 lp/mm
0.5 lp/mm
1.58 m
0.25 lp/mm
4.1 m
4.1 m
8.1 m
Plane of Focus
40 pixels across
13 line pairs
=> 45.14 lp/mm
1
2
3
1
2
3
Initial experiments suggested the optics in the camera was great

## Slide 20
1 lp/mm
0.5 lp/mm
40 pixels across
13 line pairs
=> 45.14 lp/mm
1.58 m
0.25 lp/mm
4.1 m
4.1 m
8.1 m
Plane of Focus
1
2
4
3
5
1
2
4
3
5
Initial experiments suggested the optics in the camera was great

## Slide 21
Different experimental setups in the initial stages

## Slide 22
Optical axis
10 mm
Center of entrance pupil
32 mm
Lens pivot
But that’s not how things are supposed to work. Isn’t it?
Notes: Problems ….
….From prior experience while setting up experiments for optical super-resolution in the lab, we attributed this distortion of the image to fact that the lens was not necessarily rotating about the center of the entrance pupil. Now, I haven’t explained what the entrance pupil is yet, so what is the center of the entrance pupil? Well, we will get to that in a minute. But for now, let me just say that we found this point … as shown in the figure. But, the lens in our camera always rotated about a different point. Therefore, every time we tilted the lens, the center of the entrance pupil would shift, and we had to do some adjustments—translations along the vertical and axial directions—to restore the position of the entrance pupil.
….but even when we rotated about the entrance pupil, we were observing a small shift of the image field. At that time, we weren’t really expecting this. In my prior experience during optical superresolution experiments in the lab, w The problem was we were never certain whether it was due to adjustment errors or it was for real.
…

## Slide 23
Chief rays from the object space to the image space defines the image shape
Aperture (stop)
Image plane
Optical axis
Object
Image
Chief ray
Use of similar triangles:
1

## Slide 24
Center of perspective: the chief rays from the object space converge at the center of the aperture
Aperture
Image plane
Object
Image
Chief rays
Aperture
Image plane
Object
Image
Chief rays
Notes: Furthermore, since the chief rays from the object converge at the center of the aperture, the center of the aperture is the “center of perspective projection” … in other words, if we change the location of the aperture’s center, a different set of rays from the object becomes the chief rays, and we

## Slide 25
Real lenses have several refracting surfaces on either side of the aperture (stop)
[Photograph from ilovehatephoto.com]
Cross-section of Zeiss Distagon 21mm F/2.8
Lens elements
in front of the aperture
Lens elements behind the aperture
Aperture

## Slide 26
When we look into a lens we don’t see the physical aperture, but rather an image of the aperture
+
Front view
Aperture
Entrance pupil
Marginal ray
: center of the entrance pupil
Side view
Notes: When we hold a magnifying glass over some text, the text looks magnified. Most of us will remember, the lens forms a virtual and enlarged image of the text behind the text. Similarly, when we place refracting elements in front of the aperture, we usually see a magnified image of the physical stop that is located behind the physical stop.
In the same way, when the chief rays from the

## Slide 27
The “entrance pupil” is the image of the stop formed by the front lens elements
and the “exit pupil” is the image of the stop formed by the rear lens elements
Entrance pupil
Exit pupil
Stop
Center of exit pupil ()
Center of entrance pupil ()
Chief ray
A double gauss lens (f = 102 mm) ▴
~361 mm
~144 mm
Object
Image
Aperture (stop)
Chief ray
Chief ray
Notes: Here is a widely popular lens design called the Double Gauss, with a few rays traced from the two extreme points of an object. The image shows the chief rays, the marginal rays, and the lens consisting of refracting elements in front and behind the aperture.
The zoomed in figure shows the location of the entrance pupil, which is the image of the aperture formed due to the lens elements on the object side, and the exit pupil, which is the image of the aperture formed due to the lens elements on the image side. I found the locations and the size of the images using Zemax.
Furthermore, if we concentrate on the chief rays, we can see that the chief rays from the object side entering the lens appear to converge towards the center of the entrance pupil, and the corresponding chief rays going away from the lens towards the image plane, appear to diverge from the center of the exit pupil.
Now, because the angle of the chief ray going towards the image plane will determine the height—and therefore the geometric properties—of the image, a question to ask is whether the chief ray entering the lens and and the corresponding chief ray exiting the lens are parallel?

## Slide 28
Nothing in optics makes sense except in the light of the pupils
Direction cosine
Chief ray (input)
Lens pivot & origin of camera coordinate frame
Entrance pupil
Exit pupil
Optical axis
Chief ray (output)
Pupil magnification:
2
Notes: But before we get there, lets introduce … how w
Talk about the abstraction of lens, and the pupil magnification.

## Slide 29
The pupil magnification changes the chief ray’s direction cosine
in the image space
Optical axis
Chief ray
Lens pivot & origin of camera coordinate frame
Entrance pupil
Exit pupil
Chief ray’s direction cosine at the output (image space)
Chief ray’s direction cosine at the input (object space)
,
3
Notes: The first step for building the model
.. The pivot of the lens is the center of the camera coordinate system
Notice that the output direction cosine of the chief ray is unmodified if the pupil magnification is unity.

## Slide 30
Image-object relationship for arbitrarily oriented lens and sensor rotations
Coordinates of image point in image reference frame
Coordinates of object point in camera frame
Optical axis
Chief ray
Pivots
Entrance pupil
Exit pupil
Image plane
4
Notes: … then we introduce an sensor plane, that can rotate about its independent pivot (at a distance z_o dash) from the pivot of the lens.
The pupil coordinates are highlighted in red

## Slide 31
Comparing image coordinates obtained numerically against Zemax’s ray traced values for randomly parameterized systems proved the accuracy of the model
Optical axis
Lens 2, = 30 mm
= 24.17 mm
Lens 1, = 40 mm
Exit pupil
Entrance pupil
Stop
Image plane
= -509 mm
Chief rays
Object plane
y
x
z
Lens parameters:
= -5 mm
= -25 mm
= 24 mm
= 2.0
Lens rotation parameters:
= -20°, = 10°
Sensor rotation parameters:
= 15°, = -5°

## Slide 32
World point | Computed image point | Ray-traced image point | Absolute difference
( 0.0, 0.0, -509.0) | (-0.3108, -0.6291, 0.0) | (-0.3108, -0.6291, 0.0) | (1.8e-09, 3.1e-09, 7.5e-15)
(10.0, -10.0, -509.0) | (-0.8003, -0.0863, 0.0) | (-0.8003, -0.0863, 0.0) | (2.1e-09, 2.7e-09, 3.0e-15)
(-50.0, 50.0, -509.0) | (2.1291, -3.3352, 0.0) | (2.1291, -3.3352, 0.0) | (1.2e-09, 3.2e-09, 2.9e-15)
(70.71, 70.71, -509.0) | (-4.2013, -5.0221, 0.0) | (-4.2013, -5.0221, 0.0) | (2.6e-09, 5.1e-09, 4.7e-15)
(100.0, 0.0, -509.0) | (-5.5251, -1.0101, 0.0) | (-5.5251, -1.0101, 0.0) | (1.3e-09, 8.4e-09, 3.1e-15)
( 0.0, 100.0, -509.0) | (-0.6031, -6.4387, 0.0) | (-0.6031, -6.4387, 0.0) | (2.2e-09, 4.0e-09, 2.2e-16)
(100.0, 100.0, -509.0) | (-5.8238, -6.8542, 0.0) | (-5.8238, -6.8542, 0.0) | (5.6e-10, 2.5e-10, 2.2e-15)
( 0.0, 0.0, -509.0) | (-0.3108, -0.6291, 0.0) | (-0.3108, -0.6291, 0.0) | (1.8e-09, 3.1e-09, 7.5e-15)
(10.0, -10.0, -509.0) | (-0.8003, -0.0863, 0.0) | (-0.8003, -0.0863, 0.0) | (2.1e-09, 2.7e-09, 3.0e-15)
(-50.0, 50.0, -509.0) | (2.1291, -3.3352, 0.0) | (2.1291, -3.3352, 0.0) | (1.2e-09, 3.2e-09, 2.9e-15)
(70.71, 70.71, -509.0) | (-4.2013, -5.0221, 0.0) | (-4.2013, -5.0221, 0.0) | (2.6e-09, 5.1e-09, 4.7e-15)
(100.0, 0.0, -509.0) | (-5.5251, -1.0101, 0.0) | (-5.5251, -1.0101, 0.0) | (1.3e-09, 8.4e-09, 3.1e-15)
( 0.0, 100.0, -509.0) | (-0.6031, -6.4387, 0.0) | (-0.6031, -6.4387, 0.0) | (2.2e-09, 4.0e-09, 2.2e-16)
(100.0, 100.0, -509.0) | (-5.8238, -6.8542, 0.0) | (-5.8238, -6.8542, 0.0) | (5.6e-10, 2.5e-10, 2.2e-15)
Comparing image coordinates obtained numerically against Zemax’s ray traced values for randomly parameterized systems proved the accuracy of the model
Notes: Note that Zemax doesn’t solve any alalytic equation like we did to find the image coordinates like we did. Instead, Zemax traces rays following the laws of optics, especially the vector form of Snell’s laws. Ofcourse, the roots of our model can be traced back to the snell’s laws. Therefore, we expect, if our model is accurate, the results obtained through two completely different processes should match.

## Slide 33
Image distortion due to lens rotation depends on: (a) the distance of the point of rotation from the entrance pupil center, and (b) the pupil magnification
Optical axis
Entrance pupil
Exit pupil
Image plane
Far plane
Near plane
w
w
2w
2w
-
-
Image plane
Setup
Notes: Explain the setup…
Although, a more extensive analysis is presented in the thesis, due to interest of time we are going to examine only three rows: the top, middle and bottom rows of the images from the two grids.

## Slide 34
(d)
(e)
(f)
(a)
(b)
(c)
Image distortion due to lens rotation depends on: (a) the distance of the point of rotation from the entrance pupil center, and (b) the pupil magnification
Notes: The important take away here are:
The rotation of the lens causes a shift and distortion of the image field. The exact nature of the distortion depends on the location of the lens’s pivot point with respect to the center of the entrance pupil and secondly the pupil magnification.

## Slide 35
Focusing equation for arbitrarily oriented lens and image planes
Optical axis
Chief ray
Pivots
Entrance pupil
Exit pupil
Image plane
Object plane
Object orientation:
Lens orientation: ,
Sensor orientation:
where,
;
5
Notes: Following similar steps as before, and using the constraint that the projection of any chief ray on the optical axis in the object and image side must satisfy the Gaussian equation.

## Slide 36
Focusing relations for specific configurations can be derived from the general equation: tilting a lens about its entrance pupil to focus on a tilted object plane
Lens plane
Optical axis
Image Plane
Object plane
z - axis
Entrance pupil
6
7
Notes: I have discussed few standard configurations in the thesis. There relation shown here is for the case that were are going to make use of immediately,
Verification for the specific case.

## Slide 37
The table demonstrates that the values of object plane tilt angle and image plane distance in Zemax match the numerically computed values
(Zemax)1 | (Zemax)2 | (Zemax)3 | (numerical)4 | (numerical)5
0.0° | 0.0° | 29.17073 mm | -2.2e-15° | 29.17073 mm
-10.0° | -0.46989° | 29.17145 mm | -10.0° | 29.17145 mm
25.0° | 1.24249° | 29.17572 mm | 25.0° | 29.17572 mm
-40.0° | -2.23504° | 29.18687 mm | -40.0° | 29.18687 mm
65.0° | 5.69682° | 29.27607 mm | 65.0° | 29.27607 mm
-80.0° | -14.79587° | 29.90304 mm | -80.0° | 29.90304 mm
Object plane ( mm) tilt set in Zemax. Lens plane tilt obtained using optimization using ray-tracing in Zemax. Image plane distance obtained using optimization using ray-tracing in Zemax. Object plane tilt computed numerically using the value of in column 2. Image plane distance computed numerically using the value of in column 2. |  |  |  | 
0.0° | 0.0° | 29.17073 mm | -2.2e-15° | 29.17073 mm
-10.0° | -0.46989° | 29.17145 mm | -10.0° | 29.17145 mm
25.0° | 1.24249° | 29.17572 mm | 25.0° | 29.17572 mm
-40.0° | -2.23504° | 29.18687 mm | -40.0° | 29.18687 mm
65.0° | 5.69682° | 29.27607 mm | 65.0° | 29.27607 mm
-80.0° | -14.79587° | 29.90304 mm | -80.0° | 29.90304 mm
Ray traced values (Zemax)
Numerically computed

## Slide 38
Plane of sharp focus (PoSF)
Optical axis
Depth of field (DOF)
Sensor
We can orient the plane of sharp focus & the DOF in Scheimpflug camera expedient to iris imaging
Notes: Now that we know how to orient the plane of sharp focus along a desired orientation, …..
Further to improve the transverse extent of the DOF…..
Specifically, can we take several images with different lens orientations and stitch the images together?
NOTE: I think that the wedge approximation is true for a set spatial frequency limit on the image plane …. However, if we desire a target spatial frequency in the object space, then the region is not really a wedge extending away from the camera, …. But the shape shrinks as we go from the camera.

## Slide 39
DEEP OBJECT SPACE
Sensor
Plane of sharp focus
Depth of Field
Depth of Field
Sensor
Plane of sharp focus
Depth of Field
Sensor
Plane of sharp focus
Depth of Field
Sensor
Plane of sharp focus
Depth of Field
Sensor
Plane of sharp focus
Synthesis of extended DOF in traditional photography using focus stacking
Notes: In fact there is a similar technique in conventional photography, called focus stacking.

## Slide 40
Synthesis of extended DOF in traditional photography using focus stacking
200 mm
1000 mm
200 mm
89 mm
64 mm
-axis
Sensor plane
Lens
Sensor image 1/3
Focus measure (LoG)
Sensor image 2/3
Focus measure (LoG)
Sensor image 3/3
Focus measure (LoG)

## Slide 41
Synthesis of extended DOF in traditional photography using focus stacking
Composite image
Focus measure (LoG)
Blending
Registration

## Slide 42
So here is the idea …
DEEP OBJECT SPACE
Sensor
Plane of sharp focus
Plane of sharp focus
Plane of sharp focus
Plane of sharp focus
Plane of sharp focus

## Slide 43
Notes: [Blank] But I began to wonder, why doesn’t such a method already exist?

## Slide 44
Setup of Zemax simulation to verify the theory of angular focus stacking (AFS) to extend the DOF
Sensor plane
6 x 5 sq. mm, 1.78
Lens ( =1)
Paraxial thick-lens model with spherical aberration;
= 24 mm, F/2.5
200 mm
1000 mm
200 mm
89 mm
64 mm
-axis
Sensor image 1/13 ( 0°)
1/2
1/2
Focus measure (LoG)
Lens rotated by 0° about ENPP
Setup
Sensor plane
6 x 5 sq. mm, 1.78
Lens ( =1)
Paraxial thick-lens model with spherical aberration;
= 24 mm, F/2.5
200 mm
1000 mm
200 mm
89 mm
64 mm
-axis
Sensor image 7/13 ( -8°)
1/2
1/2
Focus measure (LoG)
Lens rotated by -° about ENPP
Setup
Sensor plane
6 x 5 sq. mm, 1.78
Lens ( =1)
Paraxial thick-lens model with spherical aberration;
= 24 mm, F/2.5
200 mm
1000 mm
200 mm
89 mm
64 mm
-axis
Sensor image 13/13 (8°)
1/2
1/2
Focus measure (LoG)
Lens rotated by ° about ENPP
Setup

## Slide 45
The inter-image homography is the geometric mapping between corresponding points in the images in the angular focal stack
Sensor image 7/13 ( -8°)
1/2
Sensor image 1/13 ( 0°)
1/2
?
Notes: The question that we are interested in asking is how is one image geometrically related to another image in the stack?
… we found out that such a relation exist only if the lens is rotated about the center of the entrance pupil. Furthermore, if the pupil magnification is unity, then

## Slide 46
The focal stack of 13 images for lens tilts between -8° and 8°
Refrence image

## Slide 47
The inter-image homography is the geometric mapping between corresponding points in the images in the angular focal stack
4
For roation of a unit pupil magnification lens about the -axis by angle
Two images obtained under lens rotations and can be related as:
8
9
10
Notes: The question that we are interested in asking is how is one image geometrically related to another image in the stack?
… this is called the inter-image homography.
We found out that such a relation—the inter-image homography—exist only if the lens is rotated about the center of the entrance pupil. Furthermore, if the pupil magnification is one, then the transformation greatly simplifies to a simple scaling and transverse shift.

## Slide 48
Composite image
Focus measure (LoG)
Registration
Blending
The composite image shows the complete scene in sharp focus

## Slide 49
Notes: [Blank slide]
… preptalk about the experiment …

## Slide 50
Setup #1
Demonstration of capture volume improvement using AFS in the laboratory
180 mm, F/8
near
middle
rear
4.04 m
0.61 m
0.61 m
Camera’s view
Ø 11 mm
Artificial iris
Pattern (2 lp/mm)
mm
3.43 m
4.04 m
4.65 m

## Slide 51
Traditional image capture with large aperture results in shallow DOF
3.43 m
4.04 m
4.65 m
Aperture: F/8 Exposure time: 0.77 sec Focused on: 4.04 m DOF: approx. 30 cm (for 2 lp/mm)
Focus measure
Notes: Mention that the patches has been scaled differently to match ???

## Slide 52
Focused regions in the images detected using LoG filter shows different regions of the scene in focus
Notes: Mention that these are “registered” images in the focal stack

## Slide 53
The focused regions overlaid on intensity images shows
rotating the lens induces a rotation of the DOF in the object space

## Slide 54
AFS composite image shows DOF extended beyond 1.2 meters
Aperture: F/8 (each image) Total exposure time: 5.4 sec DOF: greater than 1.2 m (for 2 lp/mm)
3.43 m
4.04 m
4.65 m
Focus measure
Adjustment errors causes registration errors
Notes: Talk about the registration errors arising from the uncertainties of the experiment.

## Slide 55
Near (3.43 m)
Middle (4.04 m)
Far (4.65 m)
Conventional at F/8
DOF (ro) = 29 cm
AFS
DOF (ro) 1.2 m
AFS produces at least 4x more DOF than conventional imaging
for a ro = 2 lp/mm target at 4 m
Notes: Mention that the patches has been scaled differently to match ???

## Slide 56
AFS is faster than conventional capture for equivalent DOF & exposure level. Therefore, subjects are less constrained within the extended capture volume.
AFS
Total T = 5 sec.
Each T = 0.77 sec.
Conventional at F/22
T = 8 sec.
Near (3.43 m )
Middle (4.04 m )
Far (4.65 m )
Notes: Since the main comparision here is for the total time … I can probably scale the images of the eye patches

## Slide 57
Setup #2
Could we push a
4.04 m
180 mm, F/8
0.61 m
0.61 m
near
middle
rear
0.61 m
0.61 m
3.43 m
near
middle
rear
Setup #1
Camera’s view
Ø 11 mm
Artificial iris
Pattern (3.94 lp/mm)
3.43 m
4.04 m
2.82 m

## Slide 58
Near (2.82 m)
Middle (3.43 m)
Far (4.04 m)
Conventional at F/8
DOF (ro) = 12.5 cm
AFS*
DOF (ro) 1.2 m
AFS with 14 focal stack images resulted 9.8x DOF than conventional imaging
for a ro = 3.94 lp/mm target at 3.43 m
*In this example, the focal stack images, after registration, were fused using Helicon focus.
Notes: Mention that the patches has been scaled differently to match ???

## Slide 59
Automatic registration and image fusion fails if the lens is not rotated about the center of the entrance pupil
Output of Helicon focus

## Slide 60
Angular focus stacking method provides several advantages for extending the capture volume
The method is simple
Low computational complexity
Easily scalable
Allows the break free from traditional optical imaging tradeoffs of resolution, DOF and noise
Faster capture time
Notes: Advantages of focus stacking method over current methods

## Slide 61
I hope that I have been able to convince you that ….
New pair of general imaging models
  Lens and the sensor planes can freely rotate about independent pivots
  Pupil parameters enable accurate and efficient estimation of geometric image properties
A new computational imaging approach for extending the depth of field of imaging systems
Conference paper, Imaging and Applied Optics Congress 2016
  Won Best Multimedia Award ( )
Journal paper submitted to OSA Applied Optics (stage: in peer review)
Software library for automating and externally controlling optical design and simulation tasks in Zemax
Invention disclosure (stage: patent being written by a lawyer)
Notes: Original contributions again

## Slide 62
Acknowledgements
Notes: acknowledgements

## Slide 63
20%
80%
5%
1%
C’
A’
B’
▴ 3D Incoherent PSF
1300 mm
108.33 mm
100 mm, F/5
C
A
B
18 mm
25 mm
DOF
▴ Imaging system
▴ Object space
B/A/C
▾ Iris in object space
B’
B’
A’
A’
C’
C’
The DOF is a result of how the incoherent 3D PSF spreads out in space
▾ 2D PSF
▾ Image (simulation)
Notes: Briefly explain what is the main cause of this limitation (DOF)
  The impulse for the 3 configurations
  Explain the 3-D incoherent PSF – distribution of intensity at the focal region for a particular system. Stress the fact that the “shape” (or nature) of the 3-D PSF is intimately tied to the optical systems’ performance both in terms of resolution and DOF.
  The focal intensity distribution, as we shall see later, is strongly influenced by the characteristics of the aperture, which we shall call the pupil function.
  Assuming a linear system model, tell how the impulse response is obtained (slices of the 3-D intensity distribution, which is the 3D incoherent PSF)
  Explain, again, the idea of DOF – what does the “red” zone in the 3-D PSF correspond to? There is a corresponding zone in the object side where you can still get acceptable quality images.

## Slide 64
Visualizations of intensity distribution of light near the focal region

## Slide 65
Controlling the DOF by aperture size is a classical (probably bygone) method
C
A
B
18 mm
25 mm
80%
20%
5%
1%
Focal length = 100 mm
F/# = 5 (aperture = 20 mm)
▴▾ Object space ▴▾ Aperture ▴▾ 3D Incoherent PSF ▴▾ 2D PSF at focus
(DOF indicated by hor. bar)
80%
20%
5%
1%
Focal length = 100 mm
F/# = 10 (aperture = 10 mm)
Notes: It can be seen that by halving the aperture diameter (doubling the F-number, ) the DOF increased four folds, which are indicated by the red triangle markers on the horizontal axis; however, the diffraction spot-size also increased two folds consequently halving the spatial resolution.
It can be seen that by halving the aperture diameter (doubling the F-number, 𝐹#) the DOF increased four folds, which are indicated by the red triangle markers on the horizontal axis; however, the diffraction spot-size also increased two folds consequently halving the spatial resolution.

## Slide 66
◂ Variation of DOF with F/# (the curved lines are diffraction based DOF, the straight lines are geometric DOF)
◂ Spatial frequency response vs. F/#
Extending the DOF by decreasing the aperture size is not a viable solution
Notes: Loss of light implying low SNR
Loss of optical spatial resolution.

## Slide 67
The lens was removed to show the posterior surface of these structures.
Credit: Dr. Richard Kessel & Dr. Randy Kardon/Tissues & Organs/Visuals Unlimited, Inc.
Inner surface of the iris, pupil, and ciliary processes

## Slide 68
State-of-the-art iris acquisition systems

## Slide 69
Found after 17 years, in 2002.
12 years old, refugee camp, Pakistan, 1984.
[Photographs by Steve McCurry, National Geographic.]
Stable
Notes: National Geographic was able to identify and find the real name of the Afghan girl, whose iconic picture became a symbol for the plight of refugees throughout the world, after 17 years by matching the iris patterns. That story demonstrates the stability of the iris pattern.
(Her name: Sharbat Gula)

## Slide 70
The iris pattern is ideal for biometric authentication and recognition
[Photograph by Dr. Jan Drewes, jandrewes.de]

## Slide 71
Iris recognition pipeline

## Slide 74
We can concluded that.
AFS
AFS
4x
9.8x
Plemmons et. al, Wavefront coding
6x
Hsieh et. al, Wavefront coding + PTZ
3x
Yoon et. al, Wavefront coding + PTZ
3x
Venugopalan et. al, PTZ + Video
Notes: Conclusion from the slide
Two parts (horizontally separated)
Just two sets of horizontal bar plots.
Compared to conventional imaging | Compared to the state-of-the art
How much DOF extension
Better in

## Slide 75
Plane of sharp focus (PoSF)
Optical axis
Depth of field (DOF)
Sensor
Depth of field (DOF) in Scheimpflug camera
Hinge line
[Merklinger, H. M. (1996). Focusing the view camera.]

## Slide 76
Plane of sharp focus (PoSF)
Optical axis
Depth of field (DOF)
Sensor

## Slide 77
The DOF in traditional camera extends towards infinity in the directions
orthogonal to the optical axis, and beyond the field of view
Optical axis
Plane of sharp focus
Depth of field (DOF)
Sensor
Field of view
Notes: NOTE: I think that the wedge approximation is true for a set spatial frequency limit on the image plane …. However, if we desire a target spatial frequency in the object space, then the region is not really a wedge extending away from the camera, …. But the shape shrinks as we go from the camera. So would it be fair to suggest that the exact nature of the DOF depends on a set definition?

## Slide 78
Optical axis
Plane of sharp focus (PoSF)
Depth of field (DOF)
Sensor
Notes: … in fact there is axactly a