## Slide 1
Notes: [Blank slide] … preptalk about the experiment …

## Slide 2
Setup #1
Demonstration of capture volume improvement using AFS in the laboratory
180 mm, F/8
near
middle
rear
4.04 m
0.61 m
0.61 m
Camera’s view
Ø 11 mm
Artificial iris
Pattern (2 lp/mm)
mm
3.43 m
4.04 m
4.65 m

## Slide 3
Traditional image capture with large aperture results in shallow DOF
3.43 m
4.04 m
4.65 m
Aperture: F/8 Exposure time: 0.77 sec Focused on: 4.04 m DOF: approx. 30 cm (for 2 lp/mm)
Focus measure
Notes: Mention that the patches has been scaled differently to match ???

## Slide 4
Strategy for capture AFS images
180 mm, F/8 lens tilted b/w -16° & -19° in increments of 0.5° about the entrance pupil center
Notes: How to determine the angles
How to determine the image plane distance
How to determine
A line on how to restore the COP …
Empirically we found d = -5

## Slide 5
Focused regions in the images detected using LoG filter shows different regions of the scene in focus
Notes: Mention that these are “registered” images in the focal stack

## Slide 6
The focused regions overlaid on intensity images shows
rotating the lens induces a rotation of the DOF in the object space

## Slide 7
AFS composite image shows DOF extended beyond 1.2 meters
Aperture: F/8 (each image) Total exposure time: 5.4 sec DOF: greater than 1.2 m (for 2 lp/mm)
3.43 m
4.04 m
4.65 m
Focus measure
Adjustment errors causes registration errors
Notes: Talk about the registration errors arising from the uncertainties of the experiment.

## Slide 8
Near (3.43 m)
Middle (4.04 m)
Far (4.65 m)
Conventional at F/8
DOF (ro) = 29 cm
AFS
DOF (ro) 1.2 m
AFS produces at least 4x more DOF than conventional imaging
for a ro = 2 lp/mm target at 4 m
Notes: Mention that the patches has been scaled differently to match ???

## Slide 9
AFS is faster than conventional capture for equivalent DOF & exposure level. Therefore, subjects are less constrained within the extended capture volume.
AFS
Total T = 5 sec.
Each T = 0.77 sec.
Conventional at F/22
T = 8 sec.
Near (3.43 m )
Middle (4.04 m )
Far (4.65 m )
Notes: Since the main comparision here is for the total time … I can probably scale the images of the eye patches

## Slide 10
Setup #2
Could we push a
4.04 m
180 mm, F/8
0.61 m
0.61 m
near
middle
rear
0.61 m
0.61 m
3.43 m
near
middle
rear
Setup #1
Camera’s view
Ø 11 mm
Artificial iris
Pattern (3.94 lp/mm)
3.43 m
4.04 m
2.82 m

## Slide 11
Near (2.82 m)
Middle (3.43 m)
Far (4.04 m)
Conventional at F/8
DOF (ro) = 12.5 cm
AFS*
DOF (ro) 1.2 m
AFS with 14 focal stack images resulted 9.8x DOF than conventional imaging
for a ro = 3.94 lp/mm target at 3.43 m
*In this example, the focal stack images, after registration, were fused using Helicon focus.
Notes: Mention that the patches has been scaled differently to match ???

## Slide 12
Automatic registration and image fusion fails if the lens is not rotated about the center of the entrance pupil
Output of Helicon focus

## Slide 13
We can concluded that.
AFS
AFS
4x
9.8x
Plemmons et. al, Wavefront coding
6x
Hsieh et. al, Wavefront coding + PTZ
3x
Yoon et. al, Wavefront coding + PTZ
3x
Venugopalan et. al, PTZ + Video
Notes: Conclusion from the slide
Two parts (horizontally separated)
Just two sets of horizontal bar plots.
Compared to conventional imaging | Compared to the state-of-the art
How much DOF extension
Better in