## Slide 1
ALL-IN-FOCUS IMAGE CAPTURE USING LENS SWIVEL
A camera can only focus on a single plane, which is at a precise distance from a camera. Consequently, objects in front of and beyond the plane that is in sharp focus appear blurry in a photograph. The ability to capture a sharp image of objects at multiple depths is highly desirable in several applications including optical microscopy, machine vision, and surveillance imaging. We propose a new method for creating an all-in-focus photograph by processing images acquired as the lens is swiveled about a pivot point in the camera. The principal advantage of our invention over prior art is the reduced number of images needed to assemble an all-in-focus image, especially in scenarios wherein the scene depth is infinitely large. The accuracy of the model has been verified through optical ray tracing. Using this new model, we have also found the special conditions required for capturing images for all-in-focus imaging using lens swivel.
Indranil Sinharoy
Prasanna Rangarajan
Advisor: Marc Christensen
Abstract

## Slide 2
A PROBLEM
It is physically impossible for a camera to focus at multiple depths simultaneously – i.e. limited depth-of-field.
This BLURRING problem arises in all fields that employ imaging, especially in macro-photography, optical microscopy, machine vision and surveillance.
PLANE OF SHARP FOCUS
PLANE OF SHARP FOCUS

## Slide 3
PRIOR ART
Capture multiple images at different focal depths by translating the sensor plane along the optical axis.
Blend in-focus (sharp) patches from individual images following registration and appropriate scaling.
…
Source: “All in Focus Image by Focal Stacking-Input Images,” by Liu Feipeng
=
(Blended in Photoshop)
OPTICAL AXIS (OA)
y
x
z
SENSOR PLANE
PLANE-OF-SHARP-FOCUS
LENS

## Slide 4
A SOLUTION
Swivel the lens about a pivot point.
Planes-of-sharp-focus angularly sweeps the object space.
PLANE-OF-SHARP-FOCUS
OPTICAL AXIS (OA)
y
x
z
SENSOR PLANE
LENS

## Slide 5
A SIMULATION
Simulation setup (Using Zemax and Python):
Optical ray tracing
Paraxial thick-lens model with spherical aberration
Focal length = 24 mm, Aperture = F/2.5
y
x
z
SENSOR PLANE
LENS
200 mm
800 mm
200 mm

## Slide 6
A SIMULATION
Fronto-parallel (conventional) imaging. The lens focuses on each plane individually (red arrow)

## Slide 7
A SIMULATION
Lens tilt (9 images -6° to +6°)
Images formed on the sensor.
Image for lens at -6°.
Automatic detection of sharp focus region using the LoG.
▴
▴
▴
000.png (lens tilt = -6°)
Focus measure (LoG)
000.png (lens tilt = -6°)
Zone of sharp focus

## Slide 8
A SIMULATION
Composite image following image registration and scaling
Focus measure = Laplacian of Gaussian (LoG)

## Slide 9
COMPARISON (with prior art)
Advantages
Near-infinite depth-of-field with far fewer image captures
Simple reconstruction procedure (if pupil-magnification equals unity)
Limitations
If pupil-magnification is not one (most off-the-self lenses) image alignment becomes non-trivial.
Other possibilities
Selective focus and after-the-fact focusing (like Lytro)
Scene depth estimation

## Slide 10
IMAGE PLANE
OBJECT PLANE
y
x
z
Meridional Plane
OPTICAL AXIS (OA)
y
x
z
SAGITTAL Plane
Chief ray
Pivots
THE MATH
Relation between object point and corresponding image point :
Update to the Gaussian Lens Formula:

## Slide 11
THE MATH
Relation between image point and corresponding image point
for two observations (tilts of the lens):
If the pupil magnification :

## Slide 12
PUPIL MAGNIFICATION
Survey of pupil magnification

## Slide 13
MY THESIS PROBLEM
B/A/C
20%
80%
5%
1%
C’
A’
B’
B’
B’
A’
A’
1300 mm
108.33 mm
100 mm, f/5
C
A
B
18 mm
25 mm
DOF
▴ Imaging system
▴ 3D Incoherent PSF
▴ Object space
▾ Iris in object space
C’
C’
Image capture for Iris recognition with a large volume

## Slide 14
MY THESIS PROBLEM
Controlling DOF by decreasing aperture size
C
A
B
18 mm
25 mm
80%
20%
5%
1%
Focal length = 100 mm
F/# = 5 (aperture = 20 mm)
▴▾ Object space ▴▾ Aperture ▴▾ 3D Incoherent PSF ▴▾ 2D PSF at focus
(DOF indicated by hor. bar)
80%
20%
5%
1%
Focal length = 100 mm
F/# = 10 (aperture = 10 mm)