## Slide 1
Omnifocus image synthesis using lens swivel
Imaging and Applied Optics Congress 2016
Indranil Sinharoy Prasanna Rangarajan Marc P. Christensen
Lyle School of Engineering, SMU, Dallas, TX, USA.
Photonics Architecture Lab, SMU
Notes: In this paper we discuss a method to extend the depth of field of cameras by combining multiple images obtained while rotating a lens.

## Slide 2
Problem

## Slide 3
Cameras have limited Depth Of Field (DOF)
A lens cannot focus at multiple depths at a time causing parts of the image to appear blurry.
Notes: It is a common experience that a lens cannot focus at multiple depths at a time, causing parts of the image to appear blurry.

## Slide 4
Two existing methods to extend DOF
Notes: The technique presented here combines two existing methods which are briefly discussed next.

## Slide 5
Focus stacking concept
DEEP OBJECT SPACE
Sensor
Multiple photographs are captured at different focus depths.
Multiple photographs are captured at different focus depths.
The set of images in the stack collectively contains all regions of the 3D scene in focus.
Multiple photographs are captured at different focus depths.
The set of images in the stack collectively contains all regions of the 3D scene in focus.
An all-in-focus image is synthesized by selectively blending the sharply focused regions across the images in the stack.
Notes: In the first method, known as focus stacking, multiple photographs are captured at different focus depths. While no individual photograph contains the entire object space in focus, regions at different depths form sharp images in one or more photographs in the stack.
An all-in-focus image is generated by selectively blending the in-focus regions.
Variance in focal depth can be achieved either by changing the focal length or by varying the sensor plane distance as shown.

## Slide 6
Focus stacking concept
DEEP OBJECT SPACE
Sensor
Plane of sharp focus
Depth of Field

## Slide 7
Focus stacking concept
DEEP OBJECT SPACE
Sensor
Plane of sharp focus
Depth of Field

## Slide 8
Focus stacking concept
DEEP OBJECT SPACE
Sensor
Plane of sharp focus
Depth of Field

## Slide 9
Focus stacking concept
DEEP OBJECT SPACE
Sensor
Plane of sharp focus
Depth of Field

## Slide 10
Focus stacking concept
DEEP OBJECT SPACE
Sensor
Plane of sharp focus
Depth of Field
Notes: The plane of sharp focus is plane-parallel with the lens and sensor planes. Therefore, they intersect at infinity.

## Slide 11
Focus stacking example
200 mm
1000 mm
200 mm
89 mm
64 mm
-axis
Sensor plane
Lens
Scene with three playing cards frontoparallel with the camera.
Notes: As an example, consider a scene containing three playing cards at three different depths.

## Slide 12
Focus stacking example
200 mm
1000 mm
200 mm
89 mm
64 mm
-axis
Sensor image 1/3
Focus measure (LoG)
Sensor plane
Lens
Front card is in focus. In-focus regions are detected using a Laplacian of Gaussian filter.
Notes: First, only the front card is in focus. The in-focus regions are detected using a Laplacian of Gaussian operator.

## Slide 13
Focus stacking example
200 mm
1000 mm
200 mm
89 mm
64 mm
-axis
Sensor image 2/3
Focus measure (LoG)
Sensor plane
Lens
In the second image the lens is focused on the middle card.
Notes: The second image is captured while focusing on the middle card.

## Slide 14
Focus stacking example
200 mm
1000 mm
200 mm
89 mm
64 mm
-axis
Sensor image 3/3
Focus measure (LoG)
Sensor plane
Lens
Finally, an image with the rear card in focus is captured.
Notes: Finally, an image with the rear card in focus is captured.

## Slide 15
Focus stacking example
Registration
1/2
1/2
Composite image
Focus measure (LoG)
Blending
Magnification varies across the stack.
Notes: The individual images in the stack have varying magnifications. They are first registered and then blended to synthesize an all-in-focus image.

## Slide 16
Scheimpflug imaging
Ansel Adams, Collection Center for Creative Photography, University of Arizona, © 2016
Plane of sharp focus
Scheimpflug line
Lens plane
Image plane
Notes: In the second method called Scheimpflug imaging, the lens is rotated about a pivot inducing a rotation of the plane of sharp focus.
Using appropriate tilts, the plane of sharp focus can be aligned to bring portions of the foreground and background in focus.

## Slide 17
Proposed method

## Slide 18
Illustration of idea
DEEP OBJECT SPACE
Sensor
We tilt the lens about the entrance pupil while capturing images of the scene.
Notes: In our method, we tilt the lens about the entrance pupil while capturing images of the scene.

## Slide 19
DEEP OBJECT SPACE
Illustration of idea
Sensor
Plane of sharp focus

## Slide 20
DEEP OBJECT SPACE
Illustration of idea
Sensor
Plane of sharp focus

## Slide 21
DEEP OBJECT SPACE
Illustration of idea
Sensor
Plane of sharp focus

## Slide 22
Illustration of idea
DEEP OBJECT SPACE
Sensor
Plane of sharp focus

## Slide 23
Illustration of idea
DEEP OBJECT SPACE
DEEP OBJECT SPACE
Sensor
Plane of sharp focus
The plane of sharp focus and the depth of field sweeps through the scene forming regions in sharp focus across the stack which can be selectively blended.
Notes: The plane of sharp focus and the depth of field sweeps through the scene forming regions in sharp focus across the stack which can be selectively blended as discussed previously.

## Slide 24
Simulation

## Slide 25
Simulation
200 mm
1000 mm
200 mm
89 mm
64 mm
Setup in Zemax
-axis
13 tilts
between -8° & +8°
Sensor plane
6 x 5 sq. mm, 1.78
Sensor image 1/13 ( 0°)
1/2
1/2
Lens ( =1)
Paraxial thick-lens model with spherical aberration;
= 24 mm, F/2.5
Focus measure (LoG)
Notes: Here is Zemax based proof of concept simulation of our method, in which we rotate a 24 mm focal length symmetric lens about its entrance pupil.

## Slide 26
Simulation
200 mm
1000 mm
200 mm
89 mm
64 mm
Lens rotated by -° about ENPP
-axis
13 tilts
between -8° & +8°
6 x 5 sq. mm, 1.78
Sensor image 7/13 (-8°)
1/2
Focus measure (LoG)
1/2
Sensor plane
Lens ( =1)
Paraxial thick-lens model with spherical aberration;
= 24 mm, F/2.5
Notes: The image of the scene captured under lens tilt is shifted and contains portions of all three cards in focus.

## Slide 27
Simulation
200 mm
1000 mm
200 mm
89 mm
64 mm
-axis
13 tilts
between -8° & +8°
6 x 5 sq. mm, 1.78
Sensor image 13/13 (8°)
Lens rotated by ° about ENPP
1/2
1/2
Focus measure (LoG)
Sensor plane
Lens ( =1)
Paraxial thick-lens model with spherical aberration;
= 24 mm, F/2.5
Notes: The lens is tilted in both clockwise and anticlockwise directions.

## Slide 28
Simulation
200 mm
1000 mm
200 mm
89 mm
64 mm
Image stack
-axis
13 tilts
between -8° & +8°
6 x 5 sq. mm, 1.78
Sensor plane
Lens ( =1)
Notes: The stack contains 13 images obtained under uniform tilts of the lens between plus minus eight degrees.

## Slide 29
Simulation
Registration
1/2
1/2
Composite image
Focus measure (LoG)
Blending
Notes: Based on our geometric model of Scheimpflug imaging, we have derived a closed form expression of the inter-image homography that is used to register the images in the stack. Following registration, we create a composite image that contains all portions of the scene in focus.

## Slide 30
Advantages and comparison
Simple if the pupil magnification of the lens is one.
Can be used to improve the depth of field of Scheimpflug cameras.
Notes: Our method is simple and it can used to extend the depth of field of scheimpflug cameras.

## Slide 31
Model
Geometric relation of world point and image point
Inter-image homography under lens tilts about the entrance pupil
,
If pupil magnification, , the inter-image homography reduces to
Notes: While the notion of creating an all-in-focus image from multiple images under lens tilts is straightforward, our model allowed us to find the appropriate conditions under which such a method can be realized in practice. Please visit our poster for details.

## Slide 32
Additional information
For more details (including reproducible code) please visit
Open source tools used for numerical computations and plotting:
PyZDDE (Python Zemax DDE toolbox).
Python Scientific libraries – NumPy, Jupyter, Matplotlib & h5py.
indranilsinharoy.com/projects/omnifocus
Imaging and Applied Optics Congress 2016
Photonics Architecture Lab, SMU
Notes: Also refer to the link shown for additional information on the method. The IPython computational notebooks containing the Zemax simulations are also available.